## Slide 1: Raven Teleoperation - Automove
Yun Hsuan Su (Melody)

## Slide 2: ROS Node
ROS Nodes are processes that perform computation.
Each node is in charge of a different task.
Multiple nodes may cooperate to accomplish on bigger tasks.
Notes: For example, one node controls a laser range-finder, one node controls the wheel motors, one node performs localization, one node performs path planning, one Node provides a graphical view of the system, and so on. A ROS node is written with the use of a ROS client library, such as roscpp or rospy.

## Slide 3: ROS Communication
Notes: But how do they communicate with each other?

## Slide 4: ROS Communication
ROS Topic:
Based on a subscribe/publish system.
Many-to-many communication.
Data is exchanged asynchronously.
Agree on a paragraph structure – message.
Where: package_name/msg/myMessageType.msg
ROS Service:
Based on a request/response system.
Message bus between two nodes.
Data is exchanged synchronously in pairs. When a node sends out a request, it awaits a response.
The “.srv” file describes the data structures for requests and responses
Where:
package_name/srv/myServiceType.srv
Notes: the type of data published (the message) is always structured in the same way.
Nodes that subscribe/publish to the same topic
send and receive messages with the same structure.
A topic is an asynchronous communication method used for many-to-many communication.
A service meets a different kind of need; that for synchronous communication between two nodes.

## Slide 5: ROS Communication
In Raven teleoperation, we use ROS Topic.
(1) For long term stability.
(2) Make sure always taking the most recent commend.
Notes: We can bear with dropping or missing one or two

## Slide 6: ROS Topic
In Raven teleoperation, we use ROS Topic.
(1) For long term stability.
(2) Make sure always taking the most recent commend.
Publisher node: update whenever you want.
Subscriber node: retrieve the message when needed, so it will always obtain the most current updated version.
Notes: We can bear with dropping or missing one or two.
But we don’t want the entire system to stop and just wait for one message update response.

## Slide 7: ROS Topics in Raven
(1) publish to: raven_state
updates Raven state, including joint angles, robot position and orientation, joint angles… etc. (AND jacobian force in Kinetic release!!! )
In Raven teleoperation, we use ROS Topics.
There are 2 topics in the raven code:
(2) subscribe to: raven_automove
Receives raven remote control command. These commends are incremental comments of the robot tip position and orientation.
https://github.com/uw-biorobotics/raven2/tree/kinetic/msg
Notes: In respect to current state, not the absolute position/orientation control.

## Slide 8: ROS Topics in Raven
https://github.com/uw-biorobotics/raven2/tree/kinetic/msg
Raven has 2 topics:
(1) publish to: raven_state
(2) subscribe to: raven_automove
How to interact with Raven?
(1) subscribe to: raven_state
(2) publish to: raven_automove
Notes: Kind of need to construct this half of the puzzle
to interact with the raven ROS topics

## Slide 9: Teleoperation ROS Node for Raven
Construct a teleoperation ROS node.
(1) subscribe to: raven_state
(2) publish to: raven_automove
Notes: Have a sense of the current Raven robot pose,
And you want to design commend accordingly,
Then save it to raven_automove ROS topic

## Slide 10: Teleoperation ROS Node for Raven
Notes: In order for a node to be able to publish something,
And subscribe to something, we need the three components.

## Slide 11: Teleoperation ROS Node for Raven
1. message:
Add the message files to the msg folder
Add the .h files to some directory under src folder
Include them in your code:
# include “raven_2/raven_automove.h”
#include “raven_2/raven_state.h”
Notes: Another way is to clone the entire raven code down,
and include the .h file directly from the raven code.
This is to make your code cleaner

## Slide 12: Teleoperation ROS Node for Raven
1. message:
Initialize the publish/subscribe relation
ros::init(argc, argv, "AutoCircle_generator");
static ros::NodeHandle n;
RavenAutomove_publisher = n.advertise<raven_automove>("raven_automove", 1);
RavenState_subscriber = n.subscribe("ravenstate",1,&Raven_Controller::callback_raven_state,this);
The max number of messages it buffers up before beginning to throw away old ones.
Topic names
Declare publish/subscribe relation.
Callback function name.
This part of code can be found in this link:
Raven_Controller.cpp  “init_ros” function
Notes: buffer up a maximum of 1000 messages before beginning to throw away old ones.

## Slide 13: Teleoperation ROS Node for Raven
Initialize the publish/subscribe relation
ros::init(argc, argv, "AutoCircle_generator");
static ros::NodeHandle n;
RavenAutomove_publisher = n.advertise<raven_automove>("raven_automove", 1);
RavenState_subscriber = n.subscribe("ravenstate",1,&Raven_Controller::callback_raven_state,this);
2. callback function:
Define the callback function.
void Raven_Controller::callback_raven_state(raven_2::raven_state msg) {
x = msg.pos[0]; // Save the items in the msg directly by name
y = msg.pos[1];
// then you can do something with x,y. }
Callback function name.
This part of code can be found in this link:
Raven_Controller.cpp  “callback_raven_state” function
How do you know what items
are in the message?
The .msg file has all the information.

## Slide 14: Teleoperation ROS Node for Raven
2. callback function:
Define the callback function.
No need to call the callback function manually.
It will call itself, once there is an update to the ROS topic.

## Slide 15: Teleoperation ROS Node for Raven
3. publish function:
Define the publish function.
void Raven_Controller::publish_raven_automove() {
static raven_automove msg_raven_automove;
msg_raven_automove.hdr.stamp = msg_raven_automove.hdr.stamp.now();
tf::transformTFToMsg(TF_INCR[LEFT_ARM], msg_raven_automove.tf_incr[LEFT_ARM]); //tf_incr
RavenAutomove_publisher.publish(msg_raven_automove);
ros::spinOnce();}
This part of code can be found in this link:
Raven_Controller.cpp  “publish_raven_state” function
Wrap your command into message form:
Again, .msg file has all the information about items in the message structure.
Create a message object.
Like a postal stamp with current system time.
Special function to transform TF object to message item.
Trigger the publisher and subscriber node to update.

## Slide 16: Teleoperation ROS Node for Raven
3. publish function:
Define the publish function.
Do need to call the publish function manually.
This part of code can be found in this link:
Raven_Controller.cpp  “publish_raven_state” function
Notes: Usually in a while loop…
thread

## Slide 17: Teleoperation ROS Node for Raven
3. publish function:
Define the publish function.
Do need to call the publish function manually
Define publish rate!
ROS_PUBLISH_RATE = 1000 // in Hz.
This part of code can be found in this link:
Raven_Controller.cpp  “publish_raven_state” function
An upper bound to the publish rate.
Notes: Upper bound because…
Accumulate the error of the desired pose to current pose,
DAC too high? Estop.

## Slide 18: Raven Teleoperation Big Picture
1. message
2. callback function
3. publish function
Link to talker.cpp
Link
Link

## Slide 19: Trouble shooting
1. How to create your own ROS topic:
Generate your own message instead of interacting with existing ones. Link
2. ROS topic publishing but the other side not receiving:
(1) Check if topic name or message content are different.
(2) Useful tool to check active ROS Topics: Link
rostopic info /topic_name
rostopic echo /topic_name -c
rostopic list

## Slide 20: Trouble shooting
3. Working with multiple machines: Link(find the Trouble shooting section)
(1) Internet connection issue:
ping hostname_A
gedit /etc/hosts
(2) hostname settings:
// assume running on computer A
gedit ~/.bashrc // on computer A
ROS_MASTER_URL = host_A (or IP_A), ROS_IP = host_A (or IP_A)
gedit ~/.bashrc // on computer B
ROS_MASTER_URL = host_A (or IP_A), ROS_IP = host_B (or IP_B)

## Slide 21: Reference Code
1. Simple Test Code Link (originated from Danying!)
2. AutoCircle Generater Code Link
3. Raven2 most recent release Code Link

## Slide 22: Happy Thursday!
2016 . 12 . 01
Yun-Hsuan Su (Melody)